## Slide 1: Methods
LiDAR point cloud data were processed in R using the lidR package, with processing parallelised across two CPU cores.
The raw point cloud was inspected visually and duplicate points were removed. Noise filtering was applied using the Statistical Outlier Removal (SOR) algorithm (k = 10, m = 3), which was preferred over voxel-based approaches for its statistical robustness in forested environments.
Ground classification was performed using the Multiscale Curvature Classification (MCC) algorithm (scale = 1.5, curvature threshold = 0.3) via a LAScatalog tiling workflow with a 5 m buffer. MCC was selected over the Progressive Morphological Filter (PMF) due to its superior performance in structurally complex, densely vegetated stands such as eucalyptus, despite its greater computational demand. The classified point cloud was clipped to the stand boundaries using a shapefile.
A Digital Terrain Model (DTM) was generated at 2 m resolution using Kriging interpolation (k = 40 neighbours). Kriging was preferred over TIN — which introduces terrain smoothing — and IDW — which weights by distance alone without modelling spatial structure — as it adaptively models terrain variability, making it more appropriate for research applications. The DTM was masked to the study area extent.
The point cloud was height-normalised using TIN interpolation constrained to the Kriging DTM, ensuring consistency with the terrain surface, and points with negative normalised heights were removed.
The Canopy Height Model (CHM) was produced at 1 m resolution using the pit-free algorithm (Khosravipour et al., 2014) with height thresholds at 0, 2, 5, 10, 15, 20, 30, and 40 m. Post-processing applied NA-filling and mean smoothing via a 3×3 focal window. All three CHM outputs (base, filled, and smoothed) were exported as GeoTIFFs clipped to the stand boundaries.